MØKTY Black Rod Portable Aerial.

Technical Details:-

Semi-portable HF aerial, tripod mounted.

Bands Covered:-

40m, 20m, 17m, 12m, 10m, 6m

Component details:-

Whip:				Fibreglass constructed hollow telescopic whip

Length; 3200mm (10’ 6”) extended,

1050mm closed.

Whip diameter 22mm tapered to 10mm

Radiating Element:	2.0mm Dia, multi-strand copper single core,

insulated wire.

Tuning Coil:			56mm OA White PVC Waste Pipe,

12 Nr 6mm Wood dowels placed in 360°

Spaced as 13 to give double gap for clips.

Overall Dimension of former 68mm.

Coil wire, 1.45mm (15AWG) enamelled wire.

Inside coil dimension 68mm.

Coil length between 1st and last turns 125mm.

29 Turns at approx 4.46mm Centres.

Black Tap lead=	2.0mm wire 190mm Long

Red Tap lead=	2.0mm wire 440mm Long

Counterpoise:		2.0mm multi-strand single core insulated 					wire, overall length=5m.

Connected to insulator with 600mm nylon 					guy line. Secured with a tent peg.

Feed line:			RG8 Mini Coax with RF choke positioned 					178mm from feed point of aerial.

15 Turns on metal chocolate tin, 75mm Dia.